## Slide 1
Open “Displays” under “Settings”
Set Resolution “default”)
Uncheck automatic brightness
Uncheck Ture Tone
Make sure brightness is at the max (you will need to check this again before starting exp)

## Slide 2
Go to ”Color” tab
Hold “Opinion” and click “Calibrate” – this turns on expert options

## Slide 3
Continue with expert mode on

## Slide 4
There will be several screens like this. I tried this two different ways, and the luminance looks more linear if I don’t mess with anything here.

## Slide 5
Key step. Move the slider all the way to the left (to linear gamma)
On the next step, don’t mess with the white point
And the next step, don’t worry about allowing other users to use this calibration

## Slide 6
Name the profile
This will now be the color profile that is selected automatically.
Your screen is now ready
When done you can go back to your original profile, and check boxes that were previously checked (the first slide on this instruction PPT)